## Wheel Loader 980H

Description of Wheel Loader 980H :
Wheel Loader 980H is also a type of construction equipment . This Wheel Loader 980H is equipped with reliable original Cummins engine, famous original ZF wet-type axles with multi-disc limited-slip differentials, combined seal cylinder which obtains high seal performance and more reliability, dual brake valve & dual pipe full hydraulic brake and central lubrication.

Features of Wheel Loader 980H :
1. KD switch allows better efficiency & easy operation
2.Reliable ZF transmission case and Torque Converter
3.Bucket automatic leveling ability
4. It can deliver maximum traction in changing traction conditions

Technical Specification:

| Overall Dimension |
| --- |
| 1 | Length(with bucket on ground) | 8696(mm) |  |
| 2 | Width(to outside of wheels) | 3099(mm) |  |
| 3 | Bucket width | 3250(mm) |  |
| 4 | Height(To the top of the cab) | 3710(mm) |  |
| 5 | Wheel base | 3400(mm) |  |
| 6 | Tread | 2350(mm) |  |
| 7 | Min. ground clearance | 495.5(mm) |  |
| Main Technical Specification |
| 1 | Rated load | 7500(Kg) |  |
| 2 | Operating weight | 23500kg |  |
| 3 | Rated bucket capacity | 4.2(m3) |  |
| 4 | Max. breakout force | 218KN |  |
| 5 | Max. Drawing force | 222 KN |  |
| 6 | Max. dump clearance | 3220(mm) |  |
| 7 | Dump reach | 1275(mm) |  |
| 8 | Dump angle at any position | ≥45° |  |
| 9 | Digging depth(with bucket bottom horizontal) | 220(mm) |  |
| 10 | Min. turning radius |
|  | (1)Outside of bucket | 7042(mm) |  |
|  | (2)Outside of rear wheel | 6486(mm) |  |
| 11 | Pivot angle frame | 38±1° |  |
| 12 | Oscillating angle of rear axle | ±12° |  |
| 13 | Lifting time of bucket | 6.1(sec.) |  |
| 14 | Lowering time of bucket | 3.8(sec.) |  |
| 15 | Dumping time | 1.9(sec.) |  |
| 16 | Traveling speed(Km/h) |
|  | (1)1st gear (Forward/reverse) | 7.4 |  |
|  | (2)2nd gear (Forward/reverse) | 12.4 |  |
|  | (3)3rd gear (Forward/reverse) | 25.9 |  |
|  | (4)4th gear (Forward) | 37 |  |
| Diesel engine |
| 1 | Model | Original Cummins QSM11-C290 |  |
| 2 | Type | Direct injection. Turbocharged. Water cooling |  |
| 3 | Rated output | 216(Kw) |  |
| 4 | Inter-bore of cylinder/stroke | 125/147(mm) |  |
| 5 | Total exhaust of cylinder | 10.8(L) |  |
| 6 | Model of starting motor | 42MT400 |  |
| 7 | Power of start motor | 7.5(KW) |  |
| 8 | Voltage of starting motor | 24(V) |  |
| 9 | Rated speed | 2100(r/min.) |  |
| 10 | Max. Torque | 1329(N.m) |  |
| 11 | Starting type | Electric |  |
| 12 | Min. specific fuel consumption | 198(g/Kw.h) |  |
| 13 | Engine specific oil consumption | 1.0 (g/Kw.h) |  |
| 14 | Net weight | 980(Kg) |  |
| Transmission System |
| 1. Torque Converter |
| 1 | Type | 3-element.single stage |  |
| 2 | Torque ratio | 2.985 |  |
| 3 | Max. Dia. of flow path | 370(mm) |  |
| 4 | Cooling type | Pressure oil circulating |  |
| 2. Gear Box |
| 1 | Model | ZF4WG260 |  |
| 2 | Type | Power shift, spur gear constant-mesh |  |
| 3 | Gear shift position | 4 Forward and 3 reverse gears |  |
| 3. Axle and Tire |
| 1 | Type of main reducer | single stage |  |
| 2 | Gear ratio of main reducer | 4.777 |  |
| 3 | Type of final reducer | single stage planetary |  |
| 4 | Gear of ratio of final reducer | 5.167 |  |
| 5 | Total ratios | 24.685 |  |
| 6 | Size of tyre | 26.5-25 -20PR (L-3) |  |
| Working Device Hydraulic System |
| 1 | Model of oil pump(include brake pump) | P360A367(DRPAA)ZA15-6/P124A082DXZA12-85 |  |
| 2 | System pressure | 21(MPa) |  |
| 3 | Model of Muti-way directional valve | 7130-B103(HUSCO) |  |
| 4 | Model of pilot valve | 406-1044-1145(HUSCO) |  |
| 5 | (d*l)Dimension of lifting cylinder | Ф180*100*767(mm) |  |
| 6 | (D*l)Dimension of tilting cylinder | Ф210*110*550(mm) |  |
| Steering System |
| 1 | Type | Middle articulated frame. full hydraulic power |  |
| 2 | Model of steering pump | PB360A367DRZA17-6/P124ANSZA20 |  |
| 3 | Model of redirector | 150-1084 |  |
| 4 | System pressure | 17.5MPa |  |
| 5 | Dimension of steering cylinder | Ф100*50*441(mm) |  |
| Brake System |
| 1 | Type of traveling brake | Wet type multi-disc brake Dual brake valve& dual pipe, full hydraulic brake |  |
| 2 | System pressure | 16 (MPa) |  |
| 3 | Type of emergency brake | Lower pressure alarm brake |  |
| 4 | Type of parking brake | Electric control brake |  |
| Oil Capacity |
| 1 | Fuel(diesel) | 423(L) |  |
| 2 | Engine lubricating oil | 32(L) |  |
| 3 | Oil for converter and gear box | 38(L) |  |
| 4 | Oil for hydraulic system | 300(L) |  |
| 5 | Oil for driving axles(F/R) | 51(L) for each |  |

Changlin is a leading manufacturer in China to supply a wide range of construction machinery and construction equipment, including road rollers, skid steer loaders, backhoe loaders, Truck Mounted Crane , motor graders and some other engineering vehicle.