## Wheel Loader 947H

1. The 947H Wheel Loader is equipped with Dongfeng Cummins Engine.
2. The luxury cabin decoration and A/C of this wheel loader provide operator comfort.
3. This Wheel loader adopts 2 forward and 1 reverse power shift transmission.
4. The combined seal cylinder adopted by this wheel loader obtains high seal performance and more reliability.

Technical Specification:

| Overall Dimension |
| --- |
| 1 | Length (with bucket on ground) | 7070(mm) |
| 2 | Width (to the outside of wheels) | 2570(mm) |
| 3 | Bucket width | 2685(mm) |
| 4 | Height (to the top of the cab) | 3390(mm) |
| 5 | Wheel base | 2900(mm) |
| 6 | Tread | 2050(mm) |
| 7 | Min. ground clearance | 408(mm) |
| Main Technical Specification |
| 1 | Rated load | 4000(Kg) |
| 2 | Operating weight | 12850KG |
| 3 | Rated bucket capacity | 2.3(m3) |
| 4 | Max. breakout force | 134kN |
| 5 | Max. dump clearance | 2815(mm) |
| 6 | Dump reach | 1050(mm) |
| 7 | Dump angle at any position | ≥45° |
| 8 | Digging depth (with bucket bottom horizontal) | 190(mm) |
| 9 | Max. turning radius |
|  | (1) Outside of bucket | 6300(mm) |
|  | (2) Outside of rear wheel | 5730(mm) |
| 10 | Pivot angle frame | 38+1° |
| 11 | Oscillating angle of rear axle | +11° |
| 12 | Lifting time of bucket | ≤6.2(sec.) |
| 13 | Lowering time of bucket | ≤3.8(sec.) |
| 14 | Dumping time | ≤1.8(sec.) |
| 15 | Traveling speed (Km/h), 2 forward and 1 reverse |
|  | (1) 1st gear forward | 11 |
|  | (2) 2nd gear forward | 36 |
|  | (3) 1st gear reverse | 15 |
| Diesel Engine |
| 1 | Model | Dongfeng Cummins 6BTA5.9-C180 |
| 2 | Type | Direct injection. Turbocharged. Water cooling |
| 3 | Rated output | 132 (kW) |
| 4 | Inter-bore of cylinder / stroke | 102×120(mm) |
| 5 | Total exhaust of cylinder | 5.9(L) |
| 6 | Current of Alternator | 70(A) |
| 7 | Power of starting motor | 6(KW) |
| 8 | Voltage of starting motor | 24(V) |
| 9 | Rated speed | 2100(r/min) |
| 10 | Max. torque | 651(N.M)/1500rpm |
| 11 | Starting mode | Electric |
| 12 | Min. specific fuel consumption | 207(g/Kw.h) |
| 13 | Specific oil consumption of engine | 0.9-1.6(g/Kw.h) |
| 14 | Net weight | 710(kg) |
| Transmission System |
| 1. Torque Converter |
| 1 | Model | YJHSW315 |
| 2 | Type | 4-elements. Double stage |
| 3 | Torque ratio | 4 |
| 4 | Cooling type | Pressure oil circulating |
| 2. Transmission Case |
| 1 | Model | Z40-3000 |
| 2 | Type | ZF 5WG158 |
| 3 | Gear shift position | 5 forward and 3 reverse |
| 3. Axle and Tire |
| 1 | Type of main reducer | Spiral bevel gear, single stage |
| 2 | Gear ratio of main reducer | 5.286 |
| 3 | Type of final reducer | Single stage planetary |
| 4 | Gear ratio of final reducer | 4.4 |
| 5 | Total ratios | 23.258 |
| 6 | Max. drawing force | 125kN |
| 7 | Size of tire | 20.5-25-16PR |
| Working Device Hydraulic System |
| 1 | Model of oil pump | CBGj 3140 |
| 2 | System pressure | 180(kgf/cm2) |
| 3 | Model of multi-way directional valve | D32II |
| 4 | Pilot valve | DJS2-UX/UU |
| 5 | (D×L) Dimension of lifting cylinder | Ф150×80×695(mm) |
| 6 | (D×L) Dimension of tilt cylinder | Ф180×90×468(mm) |
| Steering System |
| 1 | Type | Middle articulated frame. Full-Hydraulic flow amp. Steering |
| 2 | Model of steering pump | CBGj 2063 / 1016-XF |
| 3 | Model of redirector | BZZ1-E630C+FKA-146020 |
| 4 | Model of distribution valve | FLD-F48H |
| 5 | System pressure | 14MPa |
| 6 | Dimension of steering cylinder | Ф70×40×460(mm) |
| Brake System |
| 1 | Type of traveling brake | Air over oil activate 4 wheel brake with caliper disc brake |
| 2 | Air pressure | 6-8(kgf/cm2) |
| 3 | Type of emergency brake | Automatic cutting air brake |
| 4 | Type of parking brake | Drum brake Manual control cutting-off air brake |
| Oil Capacity |
| 1 | Fuel (diesel) | 200(L) |
| 2 | Engine lubricating oil | 13.5(L) |
| 3 | Oil for converter and gear box | 45(L) |
| 4 | Oil for hydraulic system | 160(L) |
| 5 | Oil for driving axles (F/R) | 24/24(L) |
| 6 | Oil for brake | 2×1.0(L) |

Changlin Construction Machinery (Engineering Vehicle/ construction equipment), High Quality!!